## Slide 1
ECE 554
Team Tank
Sensors & Peripherals
ISA
Software
Branch Prediction
CPU Validation
CPU Architecture
ECE Capstone Open House 2024
Eric Dubberstein
Vishnu Vemuri
Ryan Dingle
Muthu Adithya Ramnarayanan
RISC-V 32 Bit base ISA
Instructions | Instructions (cont.)
LUI | SLTI
AUIPC | SLTIU
JAL | XORI
JALR | ORI
BEQ | ANDI
BNE | SLLI
BLT | SRLI
BGE | SRAI
BLTU | ADD
BGEU | SUB
LB | SLL
LH | SLT
LW | SLTU
LBU | XOR
LHU | SRL
SB | SRA
SH | OR
SW | AND
ADDI | ECALL
The ISA is the set of instructions that the CPU can execute
Completely open-sourced ISA
32 General Purpose Registers
32-bit fixed-width instructions
ECALL terminates execution
Fetch
Decode
Execute
Memory
Writeback
Pipeline Registers
PC
Instruction Memory
Data Memory Banks
Register File
ALU
Branch Resolution
Dynamic Branch Prediction
Hazard Detection Unit
Forwarding Units
Memory Mapped I/O
Instruction
Decode
Test assembly code
Verilog Functional Simulation
(OUR CPU)
Python behavioral simulation
Instruction Trace
Instruction Trace
== ?
Compare instruction trace files to determine PASS or FAIL
We implemented a pipelined processor in Verilog to realize this ISA
TODO: Muthu and Vishnu
TODO: Ryan: Fill in statistic and complete diagrams.
Strong Register
Valid Register
Strong Register
Our pipelined processor, which resolves branches in Decode, needs to flush one instruction on an incorrect branch prediction. To reduce the need to flush this instruction, we implemented dynamic branch prediction. Dynamic branch prediction “remembers” if a branch was previously taken or not.
After testing, our dynamic branch prediction resulted in a XXXX% improvement in the CPI (cycles per instruction) of our processor